## Slide 1
Optical VBB

## Slide 2: PIONEERS – WP2 goals
Design, built, integrate and test a very high performance optical vertical seismometer for the Moon.
Key driver
  Very High Performances : (self-noise below 10-11 m.s-2/sqrt(Hz) over 1mHz to 1 Hz.
  Easy to implement
  Low complexity for operation
  Easy to qualify / low risk
  Light weight / light power consumption
Technological concept
  Move from electrostatic displacement sensors to interferometer to get rid of electrostatic force limitation
  Operate in open loop to simplify the instrument and remove FB contributions. Induced risk : non-linearity.

## Slide 3: Design concept – Optical Readout
FOG expertise as a starting point
Typical PSD value of phase noise of iXblue FOG technology is:
Ƥφ = 3.10-7 rad/√Hz
In a Michelson interferometer, the difference in phase Δφ corresponding to the displacement of a mirror attached to the proof mass is given by equation:
So, FOG technology could theoretically reach a typical PSD value of displacement measurement:

## Slide 4: Design trades – Optical Readout
How to go from a »looped” interferometer (sagnac like) to the detection of a displacement of mass with a remote electronic ?

## Slide 5: Design trades – Optical Readout
Unbalanced, balanced and balanced&differential optical readout:
Simple
Semi-looped
Looped
(for different interferometer types)
Current baseline

## Slide 6: Design overview - schematic diagram

## Slide 7: Design overview - heritage
New : free space michelson
New : Mechanical oscillator

## Slide 8: Optical configuration– Insertion losses: robust set-up
Robust configuration with corner cubes + mirrors:
Aligned measurement mirror
Displacement of 5 mm

## Slide 9: Mechanical gain
Mechanical gain / Normal frequency
Mobile mass to get Brownian noise @ 5.10-12 m.s-2.Hz-1/2c
Motion range & Optical self noise
Method
Suspension : stiffness -> size
Levelling / recentering need
3 axes sensor head mass budget estimation

## Slide 10: Mechanical gain
Same performances for all configuration
Better overall mass budget for the high gain configuration

## Slide 11: Mechanical Oscillator Design
Mechanical Oscilator Type: Pendulum
=> Pivot
=> Boom (CDG offset wrt pivot) + Mass
Sensitivity Axis : Vertical
=> Horizontal Pendulum
=> Need for a spring to counter balance the weight momentum
Moon Pendulum Target :
Mobile Mass : 1Kg
Dg (centre of mass to centre of rotation distance) : 10cm
Mechanical Gain: 0,3 m / m.s-2
F0 : 0,35 Hz
Pivot
Mobile Mass
Dg
Support
Spring
Axis of sensitivity
Exemple of such configuration :
STS1 seismometer (vertical axis)
CDG

## Slide 12: Earth / Moon gravity
Earth 1.
Same proof mass
Different spring
Earth 2.
Same spring
Additional proof mass to be added for the Moon
9,81 m.s-2
1,62 m.s-2
Earth 3.
Same spring
Counterweight for Earth

## Slide 13: Accommodation - Horizontal

## Slide 14: Accommodation - Vertical

## Slide 15: Accommodation – integration

## Slide 16: Optical configuration – General principle: interferometer sensitivity
Dynamic vs sensitivity
A mirror displacement leads to a phase shift
for
reduces the displacement noise
reduces the velocity dynamics

## Slide 17: Performances budget
On the vertical

## Slide 18: Performances budget
On the horizontal

## Slide 19: Optical readout experimental validation setup
Simplified static set-up to test the electronics and feasibility
  Mirror displacement
  RIO ORION laser
  Non-optimized electronic board

## Slide 20: Optical readout experimental validation setup
Current limitations: Thermal fluctuations (long term)
Vibrations (short term)
Room temperature fluctuations
Vibrations
 Place set-up under vacuum
 Glue all optical components

## Slide 21: Road Map –
2021
Sub system validation tests
2022
2023
2024
2025
Detailed design
Prototype built & tests
TRL 6 demonstrator
Funded
TRL 4/5