## Slide 1: Requirements management

## Slide 2: Introduction
REQUIREMENTS EXPRESS NEEDS
In the whole project lifecycle, there must be careful thought to requirements – this is necessary for the success of the project.

## Slide 3: REQUIREMENT types
Functional : what function must have to satisfy the needs.
Performance : How it has to satisfy the needs
Constraints : cost, schedule, start and end dates…)
Interface : definition of physical and non physical interfaces.
Environmental : specific to the project, standards
Others : human resources, integration, …

## Slide 4: Requirements criteria
a) Clear and consistent, so easily understandable with one meaning. Capable of being met by the system being defined.
b) Correct, verified for no mistakes
c) Non ambiguous
d) Single, (subject-verb-object) if possible. Requirements must not combine, characteristics, functions or other that can be breakdown.
e) Complete – the requirement must define all information to meet the objectives of the system
f) Consistent – individual requirements must not conflict with each other
g) Traceability – requirements should be traced back to a parent/source or a baselined document or identified as a self-derived requirement
h) High level -> flexible, no indications on how to satisfy it
i) Lower level – can be verified by tests
l) Lower level - feasible, so inside physical and engineering feasibility definition and the project constraints range. The requirement must be technically achievable within the allowed schedule and budget constraints

## Slide 5: Requirements knowledge
All requirements and requirement strategy must be understood for the project success:
Origin – what is it derived from?
Solidity - How much is it necessary? Alternative exists?
Impact -
The quality or solidity of a derived or external requirement is essential in the development of a project
Is it a guesstimate ?
Does it have conservative factors added to it ?
Is it based on formal legal requirements or simple operational aspects ?

## Slide 6: Example, from PIP-II

## Slide 7: First step
Understanding the difference between fundamental, derived, and external requirements
- Fundamental Requirements or Key Performance Parameters (KPP): Technical requirements that if not achieved would be considered a fundamental failure of the project
- Derived Requirements on the project deliverables that evolve or are developed from other more fundamental requirements
Resolution (fundamental) - vibrational stability (derived)
- External Requirements (Stakeholders, Constraints). Requirements that are imposed external to the project that are not directly related to the KPPs but must be met
Example: Safety specific rules - Environmental / Safety compliance standards

## Slide 8: Second step: there is a hierarchy
Project mission
Scientific Objectives Scientific Requirements
Science/Engineering requirements
Breakdown in levels (PBS, WBS)
Engineering specification
Solutions
Baseline
Solution
(and alternatives)

## Slide 9: Example PIP II

## Slide 10: The hierarcy needs a requirements quality standard and traceability
Example: Dune. June 2015

## Slide 11: And loops….
Constraints
Schedule, legal, budget, policy, safety…..
OBJECTIVES
Requirement 1
Requirement 2
Requirement 3
.
.
.
Alternative 1
Alternative 2
Alternative 3
.
.
.
T
R
A
D
E
O
F
f
System version n
Feedback: is it coherent with..

## Slide 12: Quality process : description
Requirements management plan
With (typically):
Scope
Roles and Responsibilities
Requirements management strategy and framework
Type of requirements
Validation and review
Verification
Traceability
External Requirements
………………………………

## Slide 13: Traceability example. Metadata sheet
Tier 1 Upward Traceability (GRD) |  |  | Tier 2 Upward Traceability |  |  | FRS Existing Requirement Information |  |  | TRS Downward Traceability |  |  | Requirement Verification |  |  |  | 
T1 Document Name | T1 TC # | Tier 1 Statement | T2 Document Name | T2 TC # | Tier 2 Statement | Requirement #2 | Sub-Heading3 | Requirement Statement4 | TRS Name | TRS TC # | TRS Statement | Verification Method | Verification Document # | Verification Description | Verification Timeframe | Verification Status
No further upward traceability | None | NA | Magnet PRD | ED0010226 | Table 7.1 lists the maximum current requirements for the power supplies. | F-121.3.05-A001 | Cryogenic Magnet Power Supplies | The Power Supply System for the cold solenoid magnets in the HWR, SSR1 and SSR2 shall provide a maximum of 80 amps of DC current. | TBD | TBD | TRS has yet to be written. | Demonstration/Test | Magnet/Power Supply Commissioing Report | Verified through specification and procurement contract with vendor. Tested after installed in beam line. A subset of supplies will be tested for conformance on a dummy load. The report will contain the QPM test procedure and the switcher full voltage test procedure. | During beam commissioning | Open