## Slide 1
ET & Wind Turbines
RWTH Aachen University
Achim Stahl, May 8th, 2023
© Marco Kraan

## Slide 4
Rotor passes tower:
Reduced pressure on the tower
Excitation of oscillation
Pitch control:
Increas pressure during passage
 Reduce excitation.
status: Idea
effiziency: Unbekannt
cost: none
Pitch-Control

## Slide 5
Lattice tower: substantially lower friction to air
Less exciation
Open question:
Lattice towers for large turbines?
status: Okay
effiziency: high
cost: none
Lattice Tower
Bonus B23/150 Gittermast
150 kW

## Slide 6
Dampers between tower elements:
Absorbs energy in the vibrations
Reduces amplitude
status: Idee
effiziency: unknown
cost: < 10 %
Dampers in the Tower

## Slide 7
Two type of foundation:
„Flachgründung“  less impact
„Pfahlgründung“  higher impact
status: known
effiziency: high
cost: none
Foundation: Type

## Slide 8
Built water pools; float turbines
Negligible transmission
Problem: too expensive
status: known
effizienz: (almost) perfect
cost: too expensive
Floating Foundation

## Slide 9
Heavier fundation
(2 x the concrete)
Reduces the vibration of the ground
Can be combined with other measures.
status: first simulations
effiziency: 1,3 to 1,5
Cost: < 10 %
Foundation: Weight
Simulation, Prof. R. Schelenz

## Slide 10
Wider foundation shows less vibrations at the same mass
Additional reduction on top of increased mass.
status: Studied in miss
effiziency: ?
cost: < 10 %
Foundation: width

## Slide 11
status: Idea
effiziency: unclear
cost: 10 … 20 %
Foundation: Dampers
Dampers between
Fundation and ground

## Slide 12
status: Idea
effiziency: probably high
cost: 10 … 20 %
Active damping:
Aktive motion of mass on the base
of the tower
For example pumping of water between tanks
Problem: rather high effort

## Slide 13
status: simulation
effiziency: unclear
cost: < 10 %
Trenches
Trenches around the base stop the propagation of seismic waves.
Open question: Stops surface waves.
Does it sop bulk waves, too?

## Slide 14
status: simulation
effiziency: works only in special situations
cost: none
Interference
Destructive interference between seismic waves of different turbines.
Problem: Works only for specific wind directions, strengths, ….

## Slide 15
status: simulation
effiziency: locally varying
cost: none
Shielding by local terrain
Local topology / geology impact the proagation of the waves
Built windturbines behind local hills, valeys, etc.
Strongly dependent on local situation

## Slide 16
seismic wave
seismic sensors
wave field reconstruction
active compensation
test at DZA underground lab
Newtonian noise
Active Noise Mitigation
Status: Simulation
Effizienz: 2 bis 4
Kosten: im ET Budget
Expertise: Prof. Stahl
Aber: Störungen vermeiden ist besser als korrigieren

## Slide 17
ET & Wind Turbines
RWTH Aachen University
Achim Stahl, March 31st, 2023
© Marco Kraan
Thanks