## Slide 1
RWTH Aachen University
Achim Stahl, May, 8th, 2024
© Marco Kraan
Wind Turbines

## Slide 2
The noise
Low-frequency (cryogenic)
High-frequency (conventional)

## Slide 3
Excitation of vibrations
Frequency of rotor:
5 … 16.5 turns per min.
(0.08 … 0.28 Hz)
Rotor passes tower:
Reduced pressure on the tower
Excitation of oscillation

## Slide 4
noise from Aachen windpark; measurement by Sahar Shani-Kadmiel

## Slide 5
The noise

## Slide 6
Exclusion Regions

## Slide 7
Compatibility ?
temporal compatibility
spacial compatibility
technical compatibility

## Slide 8
Legal Study
Figure 3: Realistic Timeline
T0
+ 1,75 Jahre
Genehmigung
+ 7,5 Jahre
Baubeginn
In our opinion, it is imperative to create an organisation around the project very fast, further proceed with the investigations on all legal and permitting aspects and start the feasibility study/master plan before to submit the bid books to have a mature project.
2023
2025
2030
+ 5,5 years of tunneling
+ 2 years installation of first interferometers
+ a few years of commisioning
 until 2040 wind turbines will not interfer

## Slide 9
Compatibility ?
temporal compatibility
spacial compatibility
technical compatibility

## Slide 10
Aachen Windparks

## Slide 11
Technical Compatibility ?
reduce excitation
dampen oscillation
decrease coupling to underground

## Slide 12
Technical Compatibility
Larger / more massive foundation
Tuned mass dampers (pendulum)
Pitch control
Girder masts
Active damping
Workshop: Feb. 15th, Aachen: Identified 5 promising approaches

## Slide 13
Foundation
Shallow foundations preferred over deep foundations:
Aachen ✔
Double the mass:
30 – 50% Reduction; cost < 10%
Wider Fundations:
Reduction ?; no cost
Initial investigation by Prof. Ralf Schelenz (RWTH)
Center for Wind Power Drives
Waiting for approval of funds for a more detailed study.

## Slide 14
Tuned Mass Dampers
Very efficient
better than x 1/10
single frequency only
Cost:
design ~ 50 k€
hardware + installation ~ 20 k€
Waiting for approval of funds for
the design of one damper.

## Slide 15
Pitch Control
Increase pressure on the rotor upon passage in front of the tower
But:
Different impact point of force
Pitch control is used for other purposes (optimization of efficiency)
Reduction ?
Air pressure on the tower
Rotor blades shield the tower:
Reduced air pressure
Excitation of tower modes

## Slide 16
Active Damping
Active counter motion of masses
i.e. pumping water between tanks
Optimal location: gondola, but space?
Alternatively on the foundation
Probably a good measure; but substantial effort.
Submitted a proposal for the design of such a system (RWTH internal competition)
Partner: Prof. Heike Vallery
Chair of of Automatic Control

## Slide 17
Largely permeable to wind
Less excistation
Girder Masts
© ArcelorMittal
Laasow, Brandenburg
180 m Nabenhöhe
Maximale height?
ArcelorMittal offers towers up to 180 m:
Cheaper
Lighter
Optically transparent
Less foundation (by 60%)
Easy to transport and erect
(from their own advertisement)

## Slide 18
Wooden towers
Girder mast transparent to wind  low excitation
Wooden structurs high damping  low amplitudes low elasticity  low frequencies
Large base, point foundations  high coupling to underground?
© Hasslacher Green Tower

## Slide 19
Wooden towers
Vibrations and damping
Hasslacher is working on it
Measurements planned in Hannover
Foundation
prestudy (being awarded)
full study awaiting approval of funds.
Prototype:
Discussions with the city of Aachen.
Measurement by Hasslacher Green Tower

## Slide 20
ET & wind turbines
RWTH Aachen University
© Marco Kraan
Achim Stahl, May 8th, 2024