## Slide 1: Groundwater modelling : new results and future works
Quentin Guillemoto, Philippe Orban, Frédéric Nguyen
27/05/2025

## Slide 2: Objectives of the model
Open cross-border groundwater model for ecosystem service:
  quantify quantitative impacts of ET tunnels implantations on groundwater
  estimate groundwater inflows in tunnels
Regional hydrogeological model extent

## Slide 3: Aquifer simulated
all the aquifers are simulated until lower Famennian
aquifers considered as connected
with different hydrogeological properties
Table of hydrogeological units
Hydrogeological map. RUTHY and DASSARGUES, 2009.
Famennian (limestones-sandstones)
Cretaceous aquifers (sands, chalk)
Houiller (Namurian)
(shales, siltstones, sandstones)
Lower Famennian aquitard (siltstones)

## Slide 4: Numerical model
Feflow® hydrogeological flow model construction:
  finite element mesh
  steady flow model
  based on 2018 data
Regional database used in the model:
    groundwater water level observations, groundwater abstractions (Wallonia, Germany, The Netherlands)
    hydraulic conductivities
    topography
    geology
River network, groundwater level measurements and mesh of the finite elements model
Hydrogeological model according to regional geological model
Mesh sizes about 500 meters length

## Slide 5: Recent improvements of the model
Quantifying tunnels inflows using boundary conditions (3rd type)
Better discretization of the tunnel surfaces in the regional model.
  finer mesh near tunnels
  3D geometry imported into the regional model
New position of the ET tunnels
New position of the ET triangle

## Slide 6: Tunnel design simulated
Consideration of the grouting area
E
H=Patm
  Tunnel surrounded by ≈ 5 m of grouting area
  The hydraulic conductivity of the grouting area is adapted considering an acceptable inflow rate
5m
K ?
  Expected volumes are of the order of 10 L / 100 m /min
  (0.144 m³ / d / m)
  (i.e. 4320 m3/d over 30 km of tunnel)

## Slide 7: Tunnel design simulated
3rd type boudary condition
The 3D tunnel in the model
5.1 m
≈ 6.5m diameter tunnel surface
The inflow is simulated as:
Q = Ar(href-h)
A = relevant area (tunnel surface)
r = conductance (calculated from kg and d)
href = reference water level (atmospheric pressure)
h = current hydraulic head in groundwater
The inflow rates are linked to the conductance:
r = kg/d
Kg = grouting conductivity, d = grouting thickness
kg
kg
d

## Slide 8: Numerical model calibration
Geological unit | Lower Limit | Preferred values | Upper Limit
Cretaceous | 1.0⋅10-7 | 1.0⋅10-6 | 1.0⋅10-3
Namurian (Houiller) | 1.0⋅10-8 | 1.0⋅10-7 | 1.0⋅10-5
Visean and Tournaisian | 1.0⋅10-7 | 1.0⋅10-5 | 5.0⋅10-3
Famennian | 1.0⋅10-7 | 1.0⋅10-7 | 1.0⋅10-5
Ranges of hydraulic conductivity values estimations from expert knowledge and previous studies in the considered main geological unit allowed for the Pest estimation.
Calibration with Pest software 50 pilot points/geological layers, considering prior hydraulic conductivities.
    Optimization of the objective function

## Slide 9: Calibrated numerical model
Plot of groundwater level observations and groundwater level simulations.
Observed and simulated natural hydraulic heads
m

## Slide 10: Tunnel inflow estimations
Calculations of ET impacts considering variations of the grouting area hydraulic conductivity.
Using the optimized model (one set of calibrated hydraulic conductivity)
kg (m/s) | Q m3/d
1.00×10-8 | 45500
5.00×10-9 | 29000
1.00×10-9 | 7400
5.00×10-10 | 3800
1.00×10-10 | 776
Results of calculated inflow
Expected inflows

## Slide 11: Drawdown and tunnels inflows
15.7
15.8
12.6
20.8
Inflow values (L/100m/min) at tunnel sections
With a grouting conductivity of K= 1.00×10-9 and Q= 7400 m3/d (mean total value of 17L/100m/min)
18.1
kg (m/s) | Q m3/d
1.00×10-8 | 45500
5.00×10-9 | 29000
1.00×10-9 | 7400
5.00×10-10 | 3800
1.00×10-10 | 776
Baseflow river decreases:
Berwinne/Voer = 4.4 %
  Berwinne at Val-Dieu = 8.5 %
Gueul = 3.7 %
18.6

## Slide 12: Drawdown and tunnels inflows
Inflow values (L/100m/min) at tunnel sections
With a grouting conductivity of K= 5.00×10-10 and Q= 3800 m3/d (mean total value of 8.8L/100m/min)
kg (m/s) | Q m3/d
1.00×10-8 | 45500
5.00×10-9 | 29000
1.00×10-9 | 7400
5.00×10-10 | 3800
1.00×10-10 | 776
9.5
8.1
8.0
6.4
9.2
10.8
Baseflow river decreases:
Berwinne/Voer = 2.2%
  Berwinne at Val-Dieu =4.3%
Gueul = 1.9 %

## Slide 13: Null-Space Monte-Carlo analysis
Sensitivity analysis of the impact of groundwater levels taking into account different ranges of hydraulic conductivities
    400 sets of hydraulic conductivities that cannot be estimated on the basis of the calibration dataset (Doherty et al., 2010)
    Hydraulic conductivity sets with acceptable
Measurement objective function of the 400 NS-MC simulations

## Slide 14: Null-space Monte-Carlo
Geological zone | Mean K values (all elements) m/s | Mean variation factor [min – max] (all elements) (-) | Mean K values (around tunnels) m/s | Mean variation factor [min – max] (around tunnels) (-)
Cretace | 1.0x10-5 | 160 [5.7 – 7,499] | - | -
Houiller | 2.2x10-7 | 43 [11.2– 897] | 1.1x10-7 | 21 [14 .6 – 57.8]
Visean | 6.8x10-6 | 292 [9.1– 42889] | 3.8x10-6 | 59 [14.3 – 600]
Upper Fammenian | 4.8x10-7 | 47[5.6 – 920] | 3.9x10-7 | 42 [10.3 – 379]
Range of hydraulic conductivities simulated in the 400 NS-MC simulations
Computation of the 400 simulations considering the different scenarios
kg (m/s)
1.00×10-8
5.00×10-9
1.00×10-9
5.00×10-10
1.00×10-10
Scenarios of varying grouting hydraulic conductivity
Scenario with kg= 5 x 10-10 m/s

## Slide 15: Null-Space Monte-Carlo analysis
Calculated inflow values for the 400 NS-MC simulations
Scenario | kg (m/s) | Mean inflows (m3/d)
1 | 1.00×10-8 | 78100
2 | 5.00×10-9 | 29700
3 | 1.00×10-9 | 7396
4 | 5.00×10-10 | 3841
5 | 1.00×10-10 | 857
Ranges of inflows considering the different scenarios (grouting area conductivity)
Mean inflows calculated from the different scenarios

## Slide 16: Null-Space Monte-Carlo analysis
Sensitivity analysis of the hydraulic heads through the 400 NS-MC scenarios
Mean drawdown
With an hydraulic conductivity of the liner of 5.00×10-10

## Slide 17: Null-Space Monte-Carlo analysis
Sensitivity analysis of the hydraulic heads through the 400 NS-MC scenarios
Minimum drawdown
With an hydraulic conductivity of the liner of 5.00×10-10

## Slide 18: Conclusions & perspectives
      Results showed large impacts (>10m of drawdown) near the tunnels if hydraulic conductivity of the liner > 5×10-10 m/s. For all the scenarios, possible drawdown impacts are > 2m.
      Hydraulic conductivity (and thickness, water pressure in the drainage system) of the grouting area are important to mitigate the impact on groundwater ressources.
      Hydraulic conductivity (and thickness, water pressure in the drainage system) of the grouting area are important to mitigate the impact on groundwater ressources.
      Local model developments (VUB and Uliège) are being developed to consider more precise geological configuration around the tunnels and caverns.

## Slide 19
Thank you for your attention
Quentin Guillemoto
University of Liège
q.guillemoto@uliege.be