## Slide 1: Task Force: System Decomposition and Traceable Output Tables XV Einstein Telescope Symposium | Bologna
R. Meijer
26-05-2025

## Slide 2
Taking advantage of the Task Force organizational construct, where we worked with:
A multidisciplinary design team with both scientists and engineers
A “core team” that could take responsibility to coordinate integration work
A large group of subject matter experts to advise and support
Some light project management support
Taskforce construct allowed for subsystem integration
Task Force construct
Existing construct
People
System Decomposition
System Architecture

## Slide 3
An Integrated-System based Decomposition to capture the Task Force work
As presented by F. Sorrentino and R. Meijer at the 2024 ET Annual Event, Warsaw
Discipline-based  Integrated-system based decomposition
Lv. 1: ET  {Grouping of expert systems}  Lv. 2: All ET Suspensions  …
Lv. 1: ET  {Functional & physical partitioning}  Lv. 2: Low-Frequency Interferometer (LFI)  …
Sys. level 2: LF-Interferometer
SYS_004 (LFI)
Sys. level 3: LF-Test Mass tower
SYS_129 (LITM_Y)
(Detail view)

## Slide 4
SYS_002: Subsurface Civil Infra.
SYS_005: Technical Infra.
SYS_004: LFI
SYS_003: HFI
SYS_001: ET
Science case
SYS_xxx: …
SYS_033: LBS
SYS_026: LITM_X
System decomposition – Instrument branch example
REQ0001 - Einstein Telescope sensitivity budget
REQ0002 – HFI sensitivity budget
Lowest level of detail at the Integrated Tower (‘node’) level
 Total # of nodes considered per HF-LF pair: ~160
 Two decompositions: Triangle and 2L

## Slide 5
Capturing traceable requirements
Traceable requirements and specs are stored in 12 Output Tables
 One set for Triangle (TABs 1-6) and one for 2L (TABs 7-12) configuration
 Traceability from sensitivity curve to Civil Functional volumes
1. SYS_129 (LITM_Y)
1. Specification line root
1a. Optical Payload subsystem requirements
1b. Vacuum vessel subsystem requirements
1c. Seismic Isolation subsystem requirements

## Slide 6
TABs 1&7 (System Decomposition):
Numbered system node decomposition table –
‘Coat rack’ used by Tower Integration, Optical/Detector layout, Civil Infrastructure and ET Sensitivity Budget exercises
TABs 2&8 (Integrated Towers):
Captures categorization, design flexibility and boundary conditions of integrated tower nodes
 Suspension architecture
 Optical payload boundary conditions
 Vessel architecture and special features
 Detector layout boundary conditions
TABs 3&9 (Optical Layout):
Convert ‘old’ optical layout output tables to Taskforce context
 Subtable A: Captures high-level optical requirements at ET/LFI/HFI system level - connection to sensitivity curves
 Subtable B: Optical element and subassembly functions, positions, orientations
 Subtable C: Named optical elements and subassemblies system allocation and ‘spec-sheet’
 Subtable D: Optical flexibility demands
Task Force output tables overview

## Slide 7
TABs 4&10 (Detector Layout / Technical Infrastructure):
    As high-level REQs/SPCs: Detector space claims
    (tower scaffolding, logistics space, …)
    As named Subsystems: Noisy rooms, cleanrooms,
    select beampipe segments, Cryogenic infrastructure
TABs 5&11 (Civil Eng. Layout / Civil Functional Volumes):
    High-level engineering requirements on civil systems
    Functional contents and Excavated volume per cavern
    Functional contents and Excavated volume per tunnel
TABs 6&12 (ET Sensitivity/Noise budget):
- Sensitivity curves as requirement lines
- Noise components as specification lines
Task Force output tables overview

## Slide 8
Three-level system decomposition constructed for Task Force work
 Integrated-system based
 Approx. 250 nodes per ITF pair
 For both Triangle and 2L configurations
Requirements and specifications made traceable in Technical Annexes: Output Table sets
Summary
TAB1: System Decomposition
TAB6:
Sensitivity Budget
TAB3:
Optical Layout
TAB2: Tower Integration
TAB4:
Detector Layout
TAB5:
Civil Functional Volumes
Science Case
Sensitivity curves
Optical element positioning
Beam characteristics
Tower info: Footprint
Height
Access
ISO lvl
Space claims:
Cleanrooms
Noisy rooms
Tech Infra
Logistics
Safety
Optical element:
Type
Size
Co-location
Functions
& volumes:
Caverns
Tunnels
Attach

## Slide 9
Spare – logical connections between tables