## Slide 1: Requirements to Civil Infrastructure: Criteria and Tools used for the ETO Design Task Force
Jonathan Bratanata / NIKHEF
Maria Marsella / INFN
Wissam Wahbeh / FHNW

## Slide 2: Outline
Civil engineering criteria/principles used
Civil functional volumes – estimated excavated volumes
Cost estimation methodology
Engineering requirements that influence design and subsequently cost
Parametric tool for quick volume & cost estimation
Changes when comparing the 2024 design and 2025 Baseline Task Force update
  Key drivers and breakdown of volumes (and %change in vol./cost)

## Slide 3: Potential underground issues
3

## Slide 4: Functional Volumes and Geometrical Criteria
Infrastructure consists of:
  Caverns
  Tunnels (short access)
  TBM tunnels (main arms)
Volumes estimated using simplified civil engineering criteria.
Web viewable 3D Detector Layout(s): https://wiki.et-gw.eu/ED/WebHome
Arm cavities + recycling cavities
Laser, injection, detection, squeezing
Mechanical systems
Cooling & ventilation,
Electrical systems,
Safety systems,
Logistics
Tower base, suspensions, tower envelopes,
Scaffolding,
Clean rooms,
Auxiliary benches,
Beampipes
Logistics
Tunnel,
Caverns,
Access shafts/tunnels
Emergency exits, etc.

## Slide 5: Cavern Design Assumptions
Aspect ratio 1:2 (max width 25 m).
Arched ceiling assumed for volume calc only.
1xHeight spacing between caverns/tunnels.
Future refinements depend on geotechnical studies.

## Slide 6: Mechanized/TBM Tunnel Assumptions
Straight 10 km (Triangle) or 15 km (L) TBM tunnels.
Beamline straightness critical (laser requirement).
Assumes:
  Radius enlargement of 0.1m to account for TBM deviation/construction tolerance.
  Radius enlargement of 0.1m–0.3m for tunnel lining.
  Radius enlargement of 0.1m–0.15m for the annulus gap

## Slide 7: Limitations of Taskforce comparative analysis
Arm cavities + recycling cavities
Laser, injection, detection, squeezing
Mechanical systems
Cooling & ventilation,
Electrical systems,
Safety systems,
Logistics
Tower base, suspensions, tower envelopes,
Scaffolding,
Clean rooms,
Auxiliary benches,
Beampipes
Logistics
Tunnel,
Caverns,
Access shafts/tunnels
Emergency exits, etc.
Limitations of Taskforce comparative analysis:
Not tied to certain geographical and geological conditions
  Can only assume geological/hydrological conditions to a certain level
Excavation method is assumed
Construction planning scheme(s) not considered
Not considering optimal cavern/tunnel shape
  Assuming support system (primary and/or secondary lining, rockbolts, etc.)
Not considering access (shaft/tunnel), nor depth/position underground
Not considering additional tunnels needed for construction (e.g. connection/service tunnels for excavation of caverns)
Surface works not considered
Not fully considering safety (no personnel yet).

## Slide 8: Other Technical/Engineering requirements
Beyond Geometry
Projects must consider non-geometrical engineering criteria that impact:
  Cost
  Feasibility
  Long-term performance
Examples of non-geometrical requirements (discussion still on-going):
  Water tightness of caverns/tunnels
  Allowable water inflow levels
  Inclination limits for tunnels
  Cleanliness standards (for sensitive equipment)
  Environmental constraints (e.g., humidity, temperature, also fluxuations)
  Electrical and utility needs
  Safety and emergency access requirements
  Future-proofing (space or systems reserved for future upgrades)
Feasibility Implications:
  These factors may necessitate design changes→ Can lead to higher costs than early concept designs assumed
  To be assessed further in the local host site(s) feasibility studies

## Slide 9
Adoption of parametric design methodology leveraging 3D models of the infrastructure not merely as a means of geometrical representation but as a versatile tool to:
Compare alternative scenarios and situations.
Perform real-time analyses (e.g., costs, quantities).
Automate solution generation where feasible.
This approach enhances efficiency, adaptability, and decision-making throughout the design process.
Model-based parametric design and analysis
Parameters set 1
Real time Calculation: (Cavern Volumes, Tunnel Volumes & Lengths, Quantity of materials,.. )
Cost
Parameters set 2
Criteria to be considered
Parametric model (Flexible with constraints) Which include the layout variants
Option A
Option X
Multi objective optimization
Automatic layout and sections proposals
Comparison
Validation
Decision making
Parametric modelling
Generative design based on criteria to optimise

## Slide 10: Strategy for evaluating various layouts
Propose an initial layout and unit cost values
Calculate the corresponding estimated volume and cost
Deliver a feedback
Changes to the unit costs
Confirm
the solution
Evaluation from Experts (Local Teams & CERN).
New criteria to be considered
Layout changes
New proposals
Instrument science; other ideas
More detailed drawings
Cost estimation methodology:
Simplified approach based on excavation volume only.
  Not the exact geometrical/structural form for caverns (simplified extrusions)
Relative—not absolute—cost comparison.
Useful to screen layout options at early stage.
NOT a cost estimation of the project, It does not represent an accurate estimate of the final costs.
The real cost variations could deviate significantly from the volume variations due to the neglected factors.
It is essential to proceed with more detailed and methodologically advanced analyses to obtain reliable estimates.

## Slide 11: Estimated Excavation Volumes – 2025 Layout
Triangle Configuration
TBM tunnels: ~54.4% of total excavation volume→ Large component, but proportionally smaller than in L configuration
Caverns: ~36.6% of total→ ~3× larger than L layout due to 6 interferometers (vs. 2)
Non-TBM tunnels: ~9.0%→ Reflects additional connection complexity in triangle layout
Chart: 
| Caverns | Tunnels | TBM Tun.
Triangle | 1.0227 | 0.25045 | 1.5211
Chart: L (single instance)
| Caverns | Tunnels | TBM Tun.
L (Single instance) | 0.33083 | 0.029425 | 1.1369
Chart: 
| Triangle | L (Single instance) | L (2L)
Caverns | 1.0227 | 0.33083 | 0.66167
Tunnels | 0.25045 | 0.029425 | 0.058849
TBM Tun. | 1.5211 | 1.1369 | 2.2738
L Configuration
TBM tunnels: ~75.9% of total volume→ Indicates a tunnel-dominant layout, focused on 15 km arms (x2 for 2 sites)
Caverns: ~22.1%→ Suggests simpler/compact central infrastructure→ But requires 3 feasible geological sites for corner station & end stations
Non-TBM tunnels: ~2.0%→ Minimal auxiliary connections; simpler layout

## Slide 14: 2025 Baseline Layout vs 2024 Reference Layout - Triangle
Total excavation volume: → Reduced by 24.9% (~0.9mil m3 !!)
Total excavation cost:→ Reduced by 29%
TBM Tunnels:
  Volume reduction: 20.9%→ Main driver: Integration of LF and HF filter cavity tunnels with main arms; TBM tunnels still major cost component of excavation
Caverns
  Volume reduction: 9.7%→ Smaller volumes in many key areas (e.g. HFI tower, LF-corner station, splitting of caverns); Offset by increased cavern needs elsewhere due to configuration reshuffling (i.e. FCs)
  Smaller (even if longer) caverns often offer greater manageability → improved overall project feasibility.
Non-TBM Tunnels:
  Largest relative reduction: 62.5%→ Contributes ~11% to volume & cost savings
Chart: 
| Baseline | Baseline | 2024 Ref.
Caverns | 1.0227 | 1.0227 | 1.1325
Cav. Reduction | 0 | 0.10978 | 0
Tunnels | 0.25045 | 0.25045 | 0.66833
Tun. Reduc. | 0 | 0.41788 | 0
TBM tunnels. | 1.5211 | 1.5211 | 1.922
TBM tun. Reduc. | 0.92858 | 0.40092 | 0
-20.9%
-62.5%
-9.7%
-24.9%
-0.110 mil. m³; -2.9%
-0.418 mil. m³;
-11.2%
-0.401 mil. m³;
-10.8%

## Slide 15: 2025 Baseline Layout vs 2024 Reference Layout – L (numbers per instance)
Chart: 
| Baseline | Baseline | 2024 Ref.
Caverns | 0.33083 | 0.33083 | 0.4685
Cav. Reduction | 0 | 0.13767 | 0
Tunnels | 0.029425 | 0.029425 | 0.10281
Tun. Reduc. | 0 | 0.073387 | 0
TBM tunnels. | 1.1369 | 1.1369 | 1.4966
TBM tun. Reduc. | 0.57071 | 0.35966 | 0
-24.0%
-71.4%
-29.4%
-27.6%
-0.138 mil. m³; -6.7%
-0.073 mil. m³; -3.5%
-0.360 mil. m³;
-17.4%
Total excavation volume:→ Reduced by 27.6%
Total excavation cost:→ Reduced by 23%
TBM Tunnels
  Volume reduction: 24.0%→ Driven by integration of LF & HF filter cavities with main arms; Follows same optimization principle as Triangle configuration
Caverns
  Volume & cost reduction: Over 29%→ Indicates major improvements in central infrastructure. Result of mature design refinements (in optical layout and tower volumes),
Non-TBM Tunnels
  Reduction: Over 71%→ Contributes ~3.5% to volume & cost savings; Reflects significant layout simplification, similar to Triangle case

## Slide 16: Key Cost Drivers
Isolated Design Change Impact Analysis:
  Analyzed individual design changes on excavation volume and cost using the parametric tool.
  Applied changes one at a time to the 2025 baseline layout
1. Use of Periscopes for LF Filter Cavities
L: LF filter cavity in X arm uses 2m periscope
Triangle: LF filter cavity in X arm uses 4m periscope
High-risk technology, but major contributor to cost & volume reduction
Eliminating periscopes in LF adds:
  Triangle layout:: +0.454 mil. m³ (+16.3%)
  L layout (per instance): +0.210 mil. m³ (+14%)
2. Tower Footprint Reductions
Reverting to 2024 tower sizes leads to modest increases in excavation volume & cost
But larger caverns come with increased stability risks and construction challenges
Limitations of Volume-Based Cost Comparisons
  Construction feasibility (e.g., smaller caverns = easier, safer, more flexible) not fully captured
  Multiple smaller caverns can be better than a single large one, despite similar volume
  Design simplifications from optical layout, integrated towers, detector layout—but not fully reflected in these isolated changes

## Slide 17: Thanks!