## Slide 1
ET’s Model-Based Systems Engineering Update: Towards a Unified Systems Architecture
Einstein Telescope
XV Einstein Telescope Symposium Bologna – 27.05.2025
XV Einstein Telescope Symposium, Bologna

## Slide 2
2
Distributed development of a complex system: The Einstein Telescope
Over 1800 researchers of different disciplines all over Europe are involved
100’000 m3 of UHV
ET-LF operating at cryogenic temperatures
Large underground infrastructure complex
Detection accuracy: 10-19 m
Marco Kraan/ NIKHEF

## Slide 3
3
Model-Based Systems Engineering tackles the challenges in the development of complex systems
The subsystem interactions are unclear, and parameter influences cannot be traced
Data consistency across the Collaboration
Requirement interdependencies and relations are not traced
Future
Model-Based Systems Engineering (MBSE)
Single Point of Truth for data and parameter
Development results are stored in interconnected models
Requirements traceability from science case to component requirement
Tower
Beam pipe
Beam
Beam
Heat
Beam
Heat
Seismic noise
Current challenges
Document based development

## Slide 4
4
MBSE structures the product and connects requirements with behavior models
LCA
Model-Based Systems Engineering
Requirements
Behavior Models
Architecture
Detection accuracy
Vacuum pressure
Lifetime
Subsystem 1
Subsystem 2
Subsystem 3
System architecture
System
Subsystem 3
Subsystem 2
Subsystem 1
Product break down structure
Marco Kraan/ NIKHEF
Multi-Body-Simulation
Finite Difference Method
Finite Element Method
Heat Surrogate
Cost model

## Slide 5
5
Vacuum Beam Pipe Decomposition
[3]
[3]
[3]
[3]
[2]
The initial Use-Case for the MBSE exercise is the Vacuum Beam Pipe as designed by CERN

## Slide 6
6
Linking Requirements and Architecture
Requirements are managed on the 3DExperience Platform (near future: Jama Connect)
Synchronized to architecture tool
Linking requirements to the architecture enables requirements traceability

## Slide 7
7
Subsystem decomposition and architecture generation
Functions and functional interactions are derived from Components and Requirements
Technical Solutions that implement functions are connected and assigned with parameters
Usable by all, implemented by few
conditions
Beam
Molecules
Beam

## Slide 8
8
Subsystem decomposition and architecture generation
Functions and functional interactions are derived from Components and Requirements
Technical Solutions that implement functions are connected and assigned with parameters
Usable by all, implemented by few
conditions
Beam
Molecules
Beam
Molecules
conditions
Beam
Beam

## Slide 9
9
Subsystem decomposition and architecture generation
Functions and functional interactions are derived from Components and Requirements
Technical Solutions that implement functions are connected and assigned with parameters
Usable by all, implemented by few
conditions
Beam
Molecules
Beam
Molecules
conditions
Beam
Beam

## Slide 10
10
Using functional and logical architectures for requirements traceability
Residual Gas Noise
Logical architecture
Product
Requirements
What do we want?
Functional architecture
What does the system need to do?
What does the system look like?
How does the system do it?
Conditions
Beam
Molecules
Beam
Molecules
Beam
Beam
Conditions
Number of pumping stations
Parameter changes can be pushed from developers to the logical architecture
CAD model automatically updates when parameters change

## Slide 11
11
Verification requires integration of classified expert models into the architecture
Scope: Tube Unit
Purpose: Partial Pressures
Parameters
In: Number of pumps, dimensions, …
Out: partial pressures (pH2O, pH2, pCO,…)
Scope: Vacuum Beam Pipe
Purpose: Calculate VBP noise
Parameters
In: Partial pressures, pipe dimensions, temperature, …
Out: Noise
Model
Model
[3]
[4]

## Slide 12
12
Connecting integrated models within the architecture allows automated verification of requirements
Residual Gas Noise
Logical architecture
Requirements
Functional architecture
Conditions
Beam
Molecules
Beam
Molecules
Beam
Beam
Conditions
Purpose: Calculate VBP noise
Purpose: Partial Pressures
Product
5
[3]
[4]

## Slide 13
13
Connecting integrated models within the architecture allows automated verification of requirements
Residual Gas Noise
Logical architecture
Requirements
Functional architecture
Conditions
Beam
Molecules
Beam
Molecules
Beam
Beam
Conditions
Purpose: Partial Pressures
Purpose: Calculate VBP noise
Product
20
[3]
[4]

## Slide 14
Risks are connected to items of the architecture
Interconnection of items through the system architecture enables reaction chain analysis
Residual Gas Noise
Logical architecture
Product
Requirements
Functional architecture
Conditions
Beam
Molecules
Beam
Molecules
Beam
Beam
Conditions
Connecting Risk Management and Systems Architecture
Vacuum Leaks
14

## Slide 15
15
Risk Management – Analysis and Mitigation
Vacuum Leaks
Risk Cause:
Manufacturing defects
Leaky joints and valves
Failure in seals
Thermal expansion
Risk Impact:
Reduced vacuum quality
System contamination
Risk Assessment: Medium
Abatement Plan:
E.g. Rigorous testing and quality assurance during assembly
Mitigation-Management with Rating-Goals and Abatement Plans

## Slide 16
16
Seamless application of MBSE requires a robust toolchain integration
Jama
3DX
CATIA MAGIC
Process Composer
System Architecture Tool Parameter space
Model integration tool
Configuration Items
Requirements
Risk management
Verification
Geometry Models
CAD, Layout (BIM)?
Expert + Engineers
Satellite Models
Expert + Engineers Expert models (e.g. Matlab)
“Play button”
Model execution is possible from both Process Composer and CATIA MAGIC. However, currently only the execution in CATIA MAGIC allows the use of the parameter space. The use of the parameter space via Process Composer is planned.
Breakdown + Interfaces
Architecture
Documentation
Model integration Data exchange
Model integration Data exchange
Data exchange
Synchronize
Transfer
Existing Architectures
Already developed architectures such as PBS or high-level subsystem decompositions
Working interfaces
Interface 1 under development
Interface 2 under development
To populate the toolchain a database is necessary. There are two scenarios that need to be considered:
Existing architectures or high-level layouts, that present a top-down approach.
Existing detailed expert models that present a bottom-up approach.
The combination of both approaches yields a seamless traceability from science case to detailed components
Parallel exercise to prepare for the future: towards a scalable, professional toolchain for ET’s technical configuration

## Slide 17
17
ET’s MBSE exercise progress overview
Preparatory work (<Feb 2025)
Scope definition
Licensing
Basic Toolchain (< Jun 2025)
Method development using a mature system (Vacuum beam pipe):
  Architecture
  Risk management
  CAD models
  Expert models
Expanded toolchain (<Dec 2025)
Expand scope
  Integrated tower
  LF optical layout
Interconnect all modeled subsystems to one seamless data space
Expand toolchain to include Jama Connect
Future work (<Jun 2026)
Expand scope
  Cryopumps
  Civil tunnel
  Technical infrastructure
Advanced toolchain features
  Dashboarding
  Approval cycles
  Further Risk mitigation
  Design optimization methods

## Slide 18
Summary and Outlook
Frederik Moers
MSE, RWTH Aachen
SE: Connected Systems
frederik.moers@imse.rwth-aachen.de
Romano Meijer
NIKHEF
ETO-PO Systems Engineer
r.meijer@nikhef.nl
Potentials of MBSE approach:
Support alignment between ET subsystem developments
Ensure requirement fulfillment across the system
Support risk mitigation
Anticipating for the IV ET Annual Meeting:
Increased toolchain maturity
Expansion of MBSE approach to other subsystems:
  Integrated tower
  High-level interferometer
MBSE workshop for ET-all in autumn 2025
Summary:
Vacuum Beam Pipe implemented in MBSE exercise
System architectures enable:
  Parameter management
  Traceability analysis
  Requirements management
18

## Slide 19
Thank you!
Einstein Telescope
XV Einstein Telescope Symposium Bologna – 27.05.2025
XV Einstein Telescope Symposium, Bologna

## Slide 20
20
Sources
From now on demonstration of Use-Case content in tool:
System decomposition of the Vacuum Beam Pipe
[1] 3D printed concept of the Einstein Telescope created by Marco Kraan located at Nikhef, taken from ET-0385A-24
[2] Study of scattered light in the main arms of the Einstein Telescope gravitational wave detector
[3] ET-0005A-25: Deliverable 6.2 The Vacuum Pipe of ET
[4] ET-0007C-23: Conceptual design and noise budget of Einstein Telescope
Notes: Cad bilder,
Requirements bebildern
Animationen über folienzahl steuern
Hier nur architecture/decomposition
Wie decomposition?