## Slide 1: ET design ∩ Optimal control
Pooya Saffarieh, Nathan A. Holland, Michele Valentini, Jesse van Dongen, Alexandra Mitchell, Sander Sijtsma, Armin Numic, Abhay Karia, Wouter Hakvoort, Conor Mow-Lowry
Multi-scale optimal control for ET active seismic isolation
ET Annual meeting, Croatia, November 2025

## Slide 2
Design cycle
Active platform
ET requirement
design performance
Subsystem
(e.g suspension)

## Slide 3
Multi-scale
Cross coupling

## Slide 4
Modeling the plant and noise inputs
Forming acasual optimum and cost function
Optimisation and predicted performance
Multi scale optimal control

## Slide 5
Case study
OmniSens Softly suspended reference mass with HoQi readout on the reference mass
BRS-T360 Updated Beam Rotation Sensor (BRS) with HoQi readout and T360 seismometer.
Both configurations use same table design ( ISI ) with HoQi readout and seismic modeled noise from LNGS (Italy)

## Slide 6
Implementing optimal control
Numerical conditioning:
Acceleration domain reduces dynamic range (whiter spectra)
Sub-gradient algorithm rather than Riccati equation solver

## Slide 7
Control block schematic
Rotatation loop (Ry)
Translation loop (X)
sens: Inertial sensor noise
disp: Displacement sensor noise
dist: Disturbance sensor noise
H: Blending filter
K: Control filter
W: weighting function
z: performance output
Cross coupling from rotation to translation

## Slide 8
Formal definition acausal curve (optimum):
OmniSens acausal optimum decomposition x
displacement sensor
inertial sensor
free running plant
Fundamental limit on suppression in LTI feedback loop.

## Slide 9
Generalised plant
Cost function
weighted closed loop transfer function from input to output
Optimal control filter
Set of all filters which satisfy H-infinity criteria
H-infinity / max deviation norm
H-2 / RMS norm
Input (white noise)
Output (weighted motion)

## Slide 10
Optimization Method: Sub-Gradient Descent
Filter size and structure are predefined (a priori)
Robust to numerical noise and high dynamic range
No guarantee of reaching a global optimum
Supports complex, multi-objective cost functions
Example optimisation process:
Algorithm

## Slide 11
Results: OmniSens vs. BRS-T360
Accelaration
Velocity

## Slide 12
Summary
ET design necessiates iterative design
Each design relies on active feedback loops involving control filters
Loop structures are multi-scale and coupled
We presented a framework and a fundamental metric, acasusal optimum, which universally solves optimal control problem
We applied the method on two candidate sensor configurations: OmniSens and BRS-T360
OmniSens yeilds lower residual motion as predicted by the closed loop model
We have solved the problem of defining optimality for seismic isolation, and developed an implementation that resolves numerical noise issues. This method can be directly applied to solutions for ET and it can be readily updated for different sensors, platforms, and input seismic spectra.

## Slide 13
Abhay Karia poster presentation on OmniSens commissioning
Check out

## Slide 14
https://arxiv.org/abs/2507.15398
Details and open source code:
Thank you!